## Slide 1: Design of Catalytic Membrane Reactor for Oxidative Coupling of Methane
A. S. Chaudhari
F. Gallucci
M. van Sint Annaland
Chemical Process Intensification – Department of Chemical
Engineering and Chemistry - TU/e – The Netherlands
Technical session 3
Process Intensification, May 2, 2012

## Slide 2: Outline
Introduction
Design of catalytic membrane reactor
  Packed bed membrane reactor
  Hollow fiber catalytic membrane reactor
Results
Conclusions

## Slide 3: Introduction
Ethylene production
Production of ethylene from natural gas
Indirect conversion route (GTL)
Synthesis gas (CO, H2) via steam reforming of methane (SRM)
Fischer-Tropsch gives higher hydrocarbons
Direct conversion route
Oxidative coupling of methane (OCM) to ethylene
2 CH4 + O2 C2H4 + 2H2O

## Slide 4: Introduction contd…
Production of ethylene via oxidative coupling of methane [OCM]
2 CH4 + O2 C2H4 + 2H2O
CH4 + 2O2 CO2 + 2H2O
C2H4 + 3O2 2CO2 + 2H2O
Typical conversion-selectivity
problem
Highly exothermic
Large methane recycle
Maximum C2 yield < 30%

## Slide 5: Kinetics of OCM
Reaction scheme
Formation rates of C2H4, C2H6 and CO2 (primary reactions)
2 CH4 + ½ O2  C2H6 + H2O
n = 1.0
m = 0.352
CH4 + 2 O2  CO2 + 2 H2O
n = 0.587
m = 1
Distributive O2 feeding = membrane reactor
Notes: Aanpassen: stap voor stap
4

## Slide 6: Novel Process Design
Design a possible autothermal process in single multifunctional reactor
  Integration of exothermic OCM and endothermic steam reforming of methane (SRM)  Htot = 0
  Advantages:
    Increase methane utilization/conversion
    OCM/SRM  Ethylene/synthesis gas production
    Optimal heat integration
Present investigation

## Slide 7: Integration of OCM and SRM
  CH4 + ½ O2 → ½ C2H4 + H2O ΔHr = -140 kJ/mol
  CH4 + 2 O2 → CO2 + 2 H2O ΔHr = -801 kJ/mol
  Combustion of ethane/ethylene
  CH4 + H2O  3 H2 + CO ΔHr = 226 kJ/mol
  Reforming of ethane/ethylene

## Slide 8: Outline
Introduction
Design of catalytic membrane reactor
  Packed bed membrane reactor
  Hollow fiber catalytic membrane reactor
Results
Conclusions

## Slide 9: Possible packed bed membrane reactor configurations for only OCM
CH4 + O2
cooling
CH4 + O2
CH4
O2
Pre mixed adiabatic: very low C2 yield for the high temperature and O2 concentration
Pre mixed : low C2 yield at high O2 concentration
Distributive feeding: low C2 yield for
high temperature
CH4
O2
cooling
Distributive feeding with cooling
(Virtually isothermal):Highest yield 
Extremely complicated reactor design

## Slide 10: Packed bed membrane reactor concept
Packed Bed membrane Reactor
  Two cylindrical compartments separated by Al2O3 membrane for O2 distribution
Cooling on particle scale
SRM
OCM
Dual
function
catalyst
particle

## Slide 11: Integration on particle scale
Influencing CH4 mole flux to the particle centre
Preventing C2 mole flux to the particle centre
0
R
Complete conversion of O2 at OCM layer

## Slide 12: Numerical model: Particle scale
Kinetics from:
OCM: Stansch, Z., Mleczko, L., Baerns, M. (1997) I & ECR, 36(7), p-2568.
SRM: Nimaguchi and Kikuchi(1988). CES, 43(8), p-2295
Intraparticle reaction model
Optimize the catalyst particle
  Thickness of OCM catalytic layer
  Thickness of SRM catalytic layer
  Thickness of inert porous layer
  Diffusion properties viz. porosity and tortuosity
Advantages:
  Strong intraparticle concentration
  profiles
  Beneficial for C2 selectivity
  Vary rSRM: autothermal operation

## Slide 13: Outline
Introduction
Design of catalytic membrane reactor
  Packed bed membrane reactor
  Hollow fiber catalytic membrane reactor
Results
Conclusions

## Slide 14: Integration on single catalyst particle
Results – influence on performance
Methane consumption by dual function catalyst particle
Influence on CH4 conversion
  ~50% increase (Vs. OCM)
Reforming diffusion limited
  SRM flow = f(XCH4)
  Presence sufficient H2O
  Proportional to e/t or dSRM
Input: XCH4 = 0.4; XO2 = 0.005; XH2O = 0.5, rSRM = 0.5mm, rOCM = 0.5mm, rp = 1.5mm

## Slide 15: Integration on single catalyst particle contd…
Results – COx production
COx production
  Large contribution of SRM
  OCM contrib. low low pO2
Reforming diffusion limited
  Mainly CO production
  WGS on OCM cat  CO2
  Strong decrease by dOCM
Loss of C2 products by
reforming?
Input: XCH4 = 0.4; XO2 = 0.005; XH2O = 0.5, rSRM = 0.5mm, rOCM = 0.5mm, rp = 1.5mm

## Slide 16: Integration on single catalyst particle contd…
Losses of C2 to reforming core
  Negligible (Maximum 3% ) at reactor inlet conditions
What about the energy balance?
Input:
XCH4 = 0.4; XO2 = 0.005; XH2O = 0.5, rSRM = 0.5mm,
rp = 1.5mm

## Slide 17: Integration on single catalyst particle contd…
Results: Energy production  OCM/SRM particle Vs only OCM particle
  Variation of e/t ratio at constant rSRM:
Distributed feeding of O2  Qtot < 0.3 W  makes dual function catalysis possible
Autothermal operation is possible  e/t = 0.01-0.08
Other options: Variation of rSRM, steam concentration
Input:
XCH4=0.4; XH2O=0.5
T = 800 C; P = 150kPa; rOCM=0.25mm;
rSRM = 0.5mm
rp=1.5 mm

## Slide 18: Numerical model: Reactor scale
Two cylindrical compartments separated by -Al2O3 membrane for O2 distribution
Unsteady state heterogeneous reactor model coupled with intraparticle reaction model

## Slide 19: Results: Only OCM: Distributed feed of O2
Distributed feed of O2 (CH4/O2 = 4; Lr = 2m):
Distributed oxygen feeding  desirable
Premixed Vs distributed feeding  cooled mode  T = 1000 C Vs 800 C
Premixed Vs distributed feeding  Improved C2 yield  > 10% Vs 36%
For OCM  cooled reactor preferred with high yield of C2 (36%)

## Slide 20: Results: Reactor scale for OCM/SRM
Results – comparison of dual function process with only OCM
Non-isothermal conditions:
XCH4 = 0.3; XH2O = 0.4, CH4/O2 = 4, rp = 1.5mm; rOCM = 0.25mm
OCM adiabatic Vs rSRM = 20m
CH4 conversion:
55% Vs 62%

## Slide 21: Results: Reactor scale for OCM/SRM
Results – comparison of dual function process with only OCM
Non-isothermal conditions:
XCH4 = 0.3; XH2O = 0.4, CH4/O2 = 4, rp = 1.5mm; rOCM = 0.25mm
OCM adiabatic Vs rSRM = 20m
CH4 conversion at optimum C2 Yield:
CH4 conversion: 34% Vs 48%
Max. C2 Yield: 18% Vs 17%

## Slide 22: Results: Reactor scale for OCM/SRM
Results: OCM/SRM particle Vs only OCM
  Influence on heat production
Non-isothermal conditions:
XCH4 = 0.3; XH2O = 0.4, CH4/O2 = 4, rp = 1.5mm; rOCM = 0.25mm
OCM (adiabatic mode) Vs OCM/SRM
  Temperature decrease of 50-60 C
rSRM = 20 m  autothermal
operation possible at Lr = 1.2 m
Advantages:
Increased CH4 conversion
Nearly equal C2 production
at autothermal conditions
Disadvanges:
Complicated and expensive manufacturing of catalyst

## Slide 23: Outline
Introduction
Design of catalytic membrane reactor
  Packed bed membrane reactor
  Hollow fiber catalytic membrane reactor
Results
Conclusions

## Slide 24: Hollow fiber catalytic membrane reactor
Hollow fiber dual function catalytic membrane reactor
  Core SRM
  Outer shell OCM
Easier and less complicated manufacturing
SRM
OCM

## Slide 25: 2-D reactor model
Hollow fiber model Radial profiles
Reactor model  Hollow fiber model in series  Axial profiles

## Slide 26: Assumptions
Isobaric conditions
No interphase mass and heat transfer limitations
No radial concentration profiles in the OCM and SRM compartments
Uniform oxygen distribution

## Slide 27: Cases
Only OCM Dual function

## Slide 28: Outline
Introduction
Design of catalytic membrane reactor
  Packed bed membrane reactor
  Hollow fiber catalytic membrane reactor
Results
Conclusions

## Slide 29: Only OCM: Packed bed vs. Hollow fiber
C2 Yield
  Isothermal: Packed bed (41%) > Hollow fiber (39%)
  Adiabatic: Packed bed (18%) < Hollow fiber (21%)
Hollow fiber reactor  better heat transfer effects
Hollow Fiber Reactor (Solid line) : Fixed bed reactor (dotted line)

## Slide 30: Hollow fiber: Dual function vs. only OCM
C2 Yield:
  Isothermal: Dual function (29%) < only OCM (39%)
  Adiabatic: Dual function (29%) > only OCM (27%)
Maximum yield: CH4 conversion is 64% Vs 41% (Dual function Vs only OCM)
Dual function (Solid line) : Only OCM (dotted line)

## Slide 31: Conclusions
OCM / SRM integration in single multifunctional reactor
  Reactor performance:
  Hollow fiber catalytic membrane reactor > Packed bed membrane reactor
  Increased CH4 conversion compared to only OCM
  Simultaneous production of C2 and syngas without heat exchange equipment
Autothermal operation possible in both reactors
The models presented here could be useful to provide the guidelines for designing and improving the overall performance of the process
  Outlook
  Experimental demonstration

## Slide 32: Acknowledgments
Thijs Kemp (HF model) and Jeroen Ramakers (experiments)
Collaborations
Prof. dr. Ir. Leon Lefferts (University of Twente, Netherlands)
Financial support from NWO/ASPECT is gratefully acknowledged

## Slide 33
Thank you

## Slide 34: Recommendation
Dense Hollow fiber
In theory, 100% CH4 conversion
Distribute the SRM catalyst locally
Syngas and ethylene are separated