## Slide 1: Process Intensification through Coflore Reactors
Dr Gilda Gasparini
Process Intensification 2012
Newcastle upon Thyne
2nd May 2012

## Slide 2
AM Technology
Based in the UK
Founded in 2000
Manufacture chemical reactors
Strong focus on innovation

## Slide 3
Flow reactors – benefits compared to batch reactors
Improved yields/purity
Reduced equipment size/cost
Reduced solvent use
Increased output flexibility
Faster scale up
Improved energy efficiency
Simultaneous feed/discharge/heating/cooling
Higher heat transfer capacity
More extreme temperatures can be employed for shorter periods
Reduced reaction time
Optimum separation of reactants and products
Improved mixing
Orderly flow
Improved safety for hazardous reactions
Higher reactant concentration
Improved reaction time control
Reactor does not store reacted material

## Slide 4
Coflore design principle
CSTRs in series
Increased flexibility
Residence time
multi phase (G/L, S/L)
Low pressure drop
cheaper pump
Easy scale up
Dynamic mixing
Multistage for orderly flow

## Slide 5
High capital/maintenance cost of mechanical seals
Single mechanical seals leak product out
Double mechanical seals leak product in
High axial mixing
Long (multi impeller shafts) shafts create stability problems
Centrifugal separation problems (two phase mixtures)
Baffles are difficult to design and install
Designing dynamically mixed flow reactors
Conventional rotating stirrers are poorly suited to flow reactors

## Slide 6
Efficient radial mixing
No baffles (self baffling)
No seals or magnetic couplings
No centrifugal effects
No shaft stability problems
Coflore – Transverse Mixing

## Slide 7
Product flow
Reaction cell
Inter-stage channel
Discharge
Agitator
Feed
Lab scale
Ten reaction cells cut within a monolithic block
Coflore ACR – Lab scale

## Slide 8
Standard 100 millilitre reactor block
Standard 10 millilitre reactor block
Counter current reactor block
The bench top shaker platform can handle a range of reactor blocks
Patents pending
Coflore ACR – Lab scale

## Slide 9
Control RTD and surface to volume ratio with different diameter agitators
Interchangeable agitators for different applications and controlling cell volume
Spring agitator for two phase mixtures
Basket agitator for handling catalyst
Ceramic agitator
Hastelloy agitator
Coflore ACR – Lab scale

## Slide 10
Operating capacity - 1 to 10 litres
10 temperature control zones
High design pressure/temperature
Low pressure drop
High mixing efficiency
Industrial scale Coflore systems use the same mixing technique but the reaction cells are expanded into long tubes
Coflore ATR – Industrial scale
Patents pending
Patents pending

## Slide 11
mixing | 
Liquid homogeneous | Equivalent to static mixer at 4 m/s
L/L | Equivalent to ½ litre batch at 400 rpm
G/L | > 1 l batch at 600 rpm
G/L/S | 5 times better than 100 ml batch
Homogenous liquids
Gas/liquid mixtures
Slurries
Coflore Design - Mixing

## Slide 12
List of reactions:
Hoffman reaction
Suzuki reaction
Bourne reaction
Nitration
Polymerisations
Grignard reactions
De-hydrogenations
Bu-Li
Solid handling:
PVA particles, 50-200 µm, 30% concentration
Alumina particles, 50-200 µm, 10%
Caesium carbonate, up to 10%
Precipitation of NaCl up to 25%
Precipitation of hydroiodide salt of N-iodomorpholine
Semicarbazone synthesis
Nanoparticles clumps
Pd/Al2O3 retained in the block
Enzyme in whole cells
Crystallisation of CaCO3
Crystallisation of glycine
Coflore – Applications

## Slide 13
Browne, D., et al., Continuous Flow Processing of Slurries: Evaluation of an Agitated Cell Reactor, OPRD, 2011, 15 (3), pp 693–697
Coflore – Solid handling

## Slide 14
Coflore Design – Solid handling
Browne, D., et al., Continuous Flow Processing of Slurries: Evaluation of an Agitated Cell Reactor, OPRD, 2011, 15 (3), pp 693–697

## Slide 15
Coflore – test results
API: Gabapentin
Hofmann Degradation

## Slide 16
DL – amino acid resolution:
Production of L – amino acids and α – keto acid.
Move away from using a batch process towards a continuous system.
G/L/S system.
> 24 hours reaction time
Enzyme as a slurry, loaded on whole cells.
Biocatalytic oxidase

## Slide 17
Batch - 1 litre (400 rpm mixer)
Flow - 1 litre ATR (<120 strokes pm mixer)
1-10 litre ATR flow reactor
Biocatalytic oxidase

## Slide 18
Batch - 4 litre batch (400 rpm mixer)
Flow - 1 litre ATR (<120 strokes pm mixer)
Flow - 10 litre ATR (<120 strokes pm mixer)
(70% less oxygen)
1-10 litre ATR flow reactor
Batch - 1 litre (400 rpm mixer)
Biocatalytic oxidase

## Slide 19
1-10 litre ATR flow reactor
Biocatalytic oxidase
Continuous makes this process scalable
LCA data: 10 L continuous vs 10 1L batch cycles
88% reduction in kWh/L consumption
90% reduction in CO2 production
Energy consumption and CO2 production increase more slowly in continuous than batch
even more benefits will be achieved at larger scale

## Slide 20
Biocatalytic oxidase
10 – 80 ml ACR flow reactor

## Slide 21
Continuous crystallisation – preliminary results
Calcium carbonate crystals
CaCl2 + Na2CO3 CaCO3 + 2NaCl
ACR 100, 10 ml/min
Test run = 3 hours, consistent particle size
Tests performed by CMAC

## Slide 22
Continuous crystallisation – preliminary results
Calcium carbonate crystals
CaCl2 + Na2CO3 CaCO3 + 2NaCl
ACR 100, 10 ml/min
Test run = 3 hours, consistent particle size
Tests performed by CMAC

## Slide 23
AMT focuses
Solid handling
Work up – Counter current extraction
Pump selection – Gravity feed

## Slide 24: Thank You!
Mixing independent of throughput
Age segregation of products
Scale-ability
Multi-phase handling
From 10 ml to 10 litres volume